## Slide 1: BLE Mesh based IR AC Controller Software Design Document-Cloud & Gateway
Prepared by:-Kulasekaran
15-Feb-2024

## Slide 2
Revision History
Rev | Date | Author | Description
0.1 | 12.02.2024 | Kulasekaran | Initial Release
0.2 | 27.03.2024 | Kulasekaran | Changes to JSON Packet IDs

## Slide 3
Gateway MQTT packets
Packet Name | Packet ID | Description
Gateway Registration packet | 0 | Registers a Gateway device into BLE mesh network
Gateway Configuration packet | 1 | Sent back as ACK to cloud. Contains information about Gateway AC remote configuration
Gateway Unregistration packet | 2 | Removes a Gateway device from BLE mesh network
Gateway AC control packet | 3 | Contains AC control parameters to control an AC using Gateway
Gateway AC Locking packet | 4 | Sent back as ACK to cloud. Contains information about manual control of AC using remote
Gateway Reconfiguration packet | 5 | Puts gateway into AC remote configuration mode.
Gateway Temperature data packet | 6 | Contains temperature value as measured by the temperature sensor
Gateway Publish configuration packet | 7 | Tells the Gateway, how frequently it needs to publish temperature data information to the MQTT cloud
Gateway Heartbeat packet | 8 | Contains basic information about a Gateway that tells the cloud about its alive status
Gateway Reset MQTT packet | 9 | Disconnects Gateway from MQTT network. Resets the MQTT parameters stored in the Gateway and puts the Gateway into AP mode

## Slide 4
Node MQTT packets
Packet Name | Packet ID | Description
Node Provisioning packet | 100 | Provisions a Node device into the BLE mesh network
Node Configuration packet | 101 | Sent back as ACK to cloud. Contains information about Node AC remote configuration.
Node Unprovisioning packet | 102 | Removes a Node device from the BLE mesh network
Node AC control packet | 103 | Contains AC control parameters to control an AC using Node
Node AC Locking packet | 104 | Sent back as ACK to cloud. Contains information about manual control of AC using remote
Node Reconfiguration packet | 105 | Puts Node into AC remote configuration mode.
Node Temperature data packet | 106 | Contains temperature value as measured by the temperature sensor
Node publish configuration packet | 107 | Tells the Node, how frequently it needs to publish temperature data information to the MQTT cloud
Node Heartbeat packet | 108 | Contains basic information about a Node to let the cloud know about its alive status

## Slide 5
Miscellaneous MQTT packets
Packet Name | Packet ID | Description
Heartbeat configuration packet | 200 | Tells a Gateway/Node, how frequently it needs to send heartbeat packets to the cloud

## Slide 6
Gateway LED Indication states
LED Pattern | Description
RED + GREEN + BLUE toggle | Gateway is in MQTT configuration mode (AP mode)
Solid RED | Gateway lost connection to MQTT
RED + BLUE toggle | Gateway has not been registered into MQTT network
Slow Blinking BLUE | Gateway has entered AC remote configuration mode
Fast Blinking BLUE | Gateway has entered Teaching mode
Solid GREEN | Gateway is fully operational (Connected to MQTT, Registered into BLE Mesh, Configured as an AC remote)
Node LED Indication states
LED Pattern | Description
RED + BLUE toggle | Node is Unprovisioned
Slow Blinking BLUE | Node is provisioned, but not yet configured as AC remote
Fast Blinking BLUE | Node is in Teaching mode
Solid GREEN | Node is fully operational (Provisioned into BLE Mesh, Configured as an AC remote)

## Slide 7
Gateway - Button press types and modes
Types | Description
Single press | -
Double press | Puts the device into Teaching mode
Long press for 3 to 6 seconds | Puts the device into AC remote configuration mode
Long press for more than 8 seconds | Restarts the device
Node - Button press types and modes
Types | Description
Single press | -
Double press | Puts the device into Teaching mode
Long press for 3 to 6 seconds | Puts the device into AC remote configuration mode
Long press for more than 8 seconds | Restart the device

## Slide 8
Communication between Gateway and Node
Gateway -- -> Node | When to send
Node Provision packet (100) | Node Provision packet received from MQTT
Node Unprovision packet (102) | Node Unprovisoin packet received from MQTT
Node AC control packet (103) | Node AC control packet received from MQTT
Node Reconfiguration packet (105) | Node Reconfiguration packet received from MQTT
Node Publish configuration packet (107) | Node PublishConfiguration packet received from MQTT
Heartbeat configuration packet (200) | HeartBeat configuration packet received from MQTT
Gateway <--- Node | When to send
Provision ack (100) | Provisioning packet received from Gateway
Configuration ack (101) | Node got configured successfully
Unprovision ack (102) | Unprovisioning packet received from Gateway
AC control ack (103) | Node received AC control packet from Gateway
Locking feature ack (104) | Someone tried to control AC with manual remote
Reconfiguration ack (105) | Node received reconfiguration packet from Gateway
Temperature data ack (106) | Periodically send temperature data retrieved from sensor on Node
Publish configuration ack (107) | Node received Publish configuration packet from Gateway
Heartbeat message ack (108) | Periodically send HB messages to Gateway
Heartbeat configuration ack (200) | Node received Heartbeat configuration packet from Gateway
Packet name (JSON packet ID)

## Slide 9
PROCESS FLOW DIAGRAM
User scans QR code on the Gateway device with mobile app. Registration packet with Gateway details gets sent.
Registration packet is received. Gateway is added into network
User gets notified about the registration status.
Registration ack is sent to cloud
Gateway Registration
Configuration status ack is sent to cloud
Users gets notified regarding the configuration status of the Gateway.
Gateway Configuration
Registered gateway will listen for supported AC remotes’s button press.
Gateway Unregistration
User presses unregister button in the Mobile app for specific Gateway device
Unregistration packet is received. Gateway is removed from network
User gets notified about the Unregistration status.
Unregistration ack is sent to cloud
Cloud
Gateway
LED indication : BLUE + RED toggle
JsonPacketId : 0
JsonPacketId : 1
JsonPacketId : 2

## Slide 10
PROCESS FLOW DIAGRAM
User inputs AC control setting in the app for a particular Node and presses the control button. Control packet gets sent from cloud
Control packet is received and validated
Control ack gets sent back to the cloud
User gets notified regarding the control status.
Locking status ack is sent to the cloud and last IR command is sent to maintain the AC state
User gets notified regarding that a particular AC was controlled using remote and t
Users presses reconfigure button for a Node/Gateway. Reconfiguration packet is sent
Reconfiguration packet received and validated
Reconfiguration ack is passed to Cloud
User gets notified regarding the reconfiguration status
Gateway AC Control
Gateway AC Locking
Gateway Reconfiguration
Locking is enabled. Gateway detected that AC was controlled using remote.
Cloud
Gateway
LED indication : Blinking BLUE
JsonPacketId : 4
JsonPacketId : 5
JsonPacketId : 6

## Slide 11
PROCESS FLOW DIAGRAM
Gateway measures ambient temperature using the sensor on-board
Temperature data ack gets sent to cloud
Temperature data is received at the cloud
Locking status ack is sent. AC status is maintained if temperature limit were crossed by manual control
User gets notified regarding that a particular AC was controlled using remote and t
Heatbeat packet is sent to cloud
Heartbeat packet is received at the cloud
Gateway Temperature data
Gateway Publish configuration
Gateway Heartbeat packet
Locking is enabled. Gateway detected that AC was controlled using remote.
Cloud
Gateway
JsonPacketId : 6
JsonPacketId : 7
JsonPacketId : 8

## Slide 12
PROCESS FLOW DIAGRAM
User presses “MQTT configuration” button for a Gateway from the Mobile app. Reset MQTT configuration packet gets sent
MQTT configuration packet is received and validated
Gateway enters MQTT configuration mode. Sends back ack to the cloud
User gets notified regarding the MQTT configuration mode enter status
Reset MQTT configuration
Cloud
Gateway

## Slide 13
Gwy 1
Gwy 2
N1
N2
N3
N4
LTE
LTE
BLE
BLE
BLE
BLE
IR
IR
IR
IR
Air Conditioner
Air Conditioner
Air Conditioner
Air Conditioner
IR
Air Conditioner
IR
Air Conditioner
BLE
BLE
MQTT Broker

## Slide 14
PROCESS FLOW DIAGRAM
Cloud
Gateway
Node
User scans QR code on a Node device with mobile app. Provisioning packet with Node details gets sent.
Provisioning packet is received and verified. If valid, it is sent to the particular node.
Provisioning packet is received. Node gets provisioned and enters configuration mode.
Provisioning ack is sent to gatewa. (Provisioned node will wait in config mode until configured)
Received provisioning ack from Node and is sent to cloud
Users gets notified regarding the Provisioning status.
While node is waiting in Config mde, a supported AC remote’s button is pressed in front of Node’s receiver
Node detects the IR protocol and gets configured. Sends this information to Gateway
Configuration status information received from Node and sent to cloud.
Users gets notified regarding the configuration status of the node.
Node Provisioning
Node Configuration
User presses unprovision button for specific node on the mobile app
Unprovisioning packet is received and verified. If valid, it is sent to the particular node.
Unprovisioning packet is received. Node gets removed from the network
Unprovisioning ack is sent to gateway
Received Unprovisioning ack from Node and is sent to cloud
Users gets notified regarding the Unprovisioning status.
Node Unprovisioning
JsonPacketId : 100
JsonPacketId : 101
JsonPacketId : 102

## Slide 15
Cloud
Gateway
Node
PROCESS FLOW DIAGRAM
User inputs AC control setting in the app for a particular Node and presses the control button. Control packet gets sent from cloud
Control packet is received and if valid, it is sent to Node.
Node receives the control packet and controls the AC. Sends back Ack to the Gateway
If control packet was invalid, ack with error code gets sent to cloud
User gets notified regarding the control status.
If invalid
Locking is enabled. Node detected that AC was controlled using remote.
Sends this information to Gateway. Also sends back previous IR command to maintain the AC’s locked state.
Gateway receives the locking status info from Node and sends it to cloud
User gets notified regarding that a particular AC was controlled using remote and t
Users presses reconfigure button for a Node/Gateway. Reconfiguration packet is sent
Reconfiguration packet received and if valid, it is sent to Node.
Reconfiguration packet is received. Node enters Configuration mode.
Reconfiguraion ack is sent.
Reconfiguration ack is received. Ack is passed to Cloud
User gets notified regarding the reconfiguration status
Node AC Control
Node Locking
Node Reconfiguration
JsonPacketId : 103
JsonPacketId : 104
JsonPacketId : 105

## Slide 16
Cloud
Gateway
Node
PROCESS FLOW DIAGRAM
Node measures ambient temperature using on-board temperature sensor
Gateway receives Node temperature data ack and sends it to cloud
Node temperature data ack is received at cloud
Node sends publish configuration ack to Gateway
Gateway receives Node publish configuration ack and sends it to cloud
Node publish configuration ack received at cloud
Node Heartbeat ack is sent to Gateway
Node Heartbeat ack is received by Gateway and sent to cloud
Node Heartbeat ack is received at cloud
Node Temperature data
Node Publish configuration
Node Heartbeat
JsonPacketId : 106
JsonPacketId : 107
JsonPacketId : 108
Node sends temperature data ack to Gateway
User configures Node’s publishing information. Node Publish configuration packet is sent to Gateway
Node Publish configuration packet is received and if valid, sent to Node
Node publish configuration packet is received. This will set how frequenty Temperature data needs to be sent to gateway

## Slide 17
Gateway
Gateway Registration
LTE
Key | Value | Type | Range
JsonPacketId | 0 | Number | 0 - 99
MsgSeqNo | 12 | Number | 0 - 65535
GwySerNo | 00001 | Number | 0 - 65535
Location | "1st floor" | String | 20 char long
Gateway Registration Packet
Key | Value | Type | Range
JsonPacketId | 0 | Number | 0 - 99
MsgSeqNo | 12 | Number | 0 - 65535
GwySerNo | 00001 | Number | 0 - 65535
Location | "1st floor" | String | 20 char long
Error Code | 0 | Number | 0 - 3
Gateway Registration Ack
Json packet (Cloud -> Gateway)
{
"JsonPacketId" : 0,
"MsgSeqNo": 12,
"GwySerNo": "GWY00005",
"location": “1st Floor"
}
Cloud
1. Gateway Registration packet sent from Cloud to Gwy
2. Gwy sends back Gateway registration Ack
Json ack (Gateway -> Cloud)
{
"JsonPacketId" : 0,
"MsgSeqNo": 12,
"GwySerNo": "GWY00005",
"location": “1st Floor",
"Errorcode": 0
}
Gateway registration is the process of adding a gateway into the BLE Mesh network.
Using the Mobile app, user will scan the QR code sticker placed on the Gateway device. The app will extract necessary information from QR code and send the Gateway Registration packet to Gateway via MQTT cloud

## Slide 18
Gateway
Cloud
LTE
Gateway Configuration
1. Gateway sends configuration status ack to cloud
Key | Value | Type | Range
JsonPacketId | 1 | Number | 0 - 99
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ErrorCode | 0 | Number | 0 - 6
Configuration status
Error code | Meaning
0 | Success
1 | Invalid GwySerNo
2 | Invalid NodeSerNo
Error codes
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 1,
"GwySerNo": 2,
"Errorcode" : 0
}
Gateway Configuration is the process in which the node is set to use a specific protocol for controlling the Air conditioner.
A registered unconfigured gateway will be waiting in configuration mode until configured.
When a supported AC remote button is pressed in front of the Gateway’s receiver, the gateway will get configured to act as that AC remote.

## Slide 19
Gateway Unregistration
Gateway
Key | Value | Type | Range
jsonPacketId | 2 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 00001 | Number | 0 - 65535
Location | "1st floor" | String | 20 char long
Un-Registration Packet
Key | Value | Type | Range
JsonPacketId | 2 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 00001 | Number | 0 - 65535
Location | "1st floor" | String | 20 char long
Error Code | 0 | Number | 0 - 3
Un-Registration Packet Ack
Cloud
1. Unregistration Json packet sent from Cloud to Gwy
2. Gwy sends back UnRegistration Ack back to cloud
Json packet (Cloud -> Gateway)
{
"JsonPacketId" : 2,
"MsgSeqNo": 12,
"GwySerNo": "GWY00005",
"location": "ABCD Showroom"
}
LTE
Json ack (Cloud -> Gateway)
{
"JsonPacketId" : 2,
"MsgSeqNo": 12,
"GwySerNo": "GWY00005",
"location": "ABCD Showroom",
"Errorcode": 0,
}
Gateway Unregistration is the process of removing a gateway from the Mesh network.

## Slide 20
Gateway
Cloud
LTE
Gateway AC Control
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 3,
"MsgSeqNo": 1,
"GwySerNo": 2,
"Power": 1,
"Mode": "Cool",
"Fan": 5,
"Temp": 25,
"SwingH": 1,
"SwingV": 1,
"OnTimer": 0,
"OffTimer": 0,
"Locking": 1
}
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 3,
"MsgSeqNo": 1,
"GwySerNo": 2,
"Power": 1,
"Mode": "Cool",
"Fan": 5,
"Temp": 25,
"SwingH": 1,
"SwingV": 1,
"OnTimer": 0,
"OffTimer": 0,
"Locking": 1,
"Errorcode": 0,
}
1. Control packet is sent from the cloud
2. Gateway sends control ack back to cloud

## Slide 21
Key | Value | Type | Range
JsonPacketId | 3 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 – 65535
GwySerNo | 1 | Number | 0 – 65535
Power | 1 = ON, 0 = OFF | Number | 0, 1
Mode | "Cool" | String | "Cool", "Hot", "Dry", "Auto", "Quiet"
Fan | 2 | Number | 0 – 4
Temperature | 25 | Number | 16 - 32
SwingH | 1 = ON, 0 = OFF | Number | 0, 1
SwingV | 1 = ON, 0 = OFF | Number | 0, 1
OnTimer | 4 | Number | 0 – 12
OffTimer | 5 | Number | 0 – 12
Locking | 1 = ON, 0 = OFF | Number | 1, 0
Control packet
Key | Value | Type | Range
JsonPacketId | 3 | Number | 0 – 99
MsgSeqNo | 1 | Number | 0 – 65535
GwySerNo | 1 | Number | 0 – 65535
Power | 1 = ON, 0 = OFF | Number | 0, 1
Mode | "Cool" | String | "Cool", "Hot", "Dry", "Auto", "Quiet"
Fan | 2 | Number | 0 – 4
Temperature | 25 | Number | 16 - 32
SwingH | 1 = ON, 0 = OFF | Number | 0, 1
SwingV | 1 = ON, 0 = OFF | Number | 0, 1
OnTimer | 4 | Number | 0 – 12
OffTimer | 5 | Number | 0 – 12
Locking | 1 = ON, 0 = OFF | Number | 1, 0
ErrorCode | 0 | Number | 0 - 15
Control ack
Error code | Meaning
0 | Success
1 | Invalid GwySerNo
4 | Invalid Power
5 | Invalid Mode
6 | Invalid Fan speed
7 | Invalid Temperature
8 | Invalid SwingH
9 | Invalid SwingV
10 | Invalid OnTimer
11 | Invalid OffTimer
12 | Invalid Locking
Error codes

## Slide 22
Gateway
Cloud
LTE
Gateway AC Locking
1. Gateway detects that AC got controlled by its remote and Locking feature is enabled.
Key | Value | Type | Range
JsonPacketId | 4 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 – 65535
GwySerNo | 1 | Number | 0 – 65535
Locking status
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 4,
"MsgSeqNo": 1,
"GwySerNo": 2,
}
Gateway sends back previous IR command to bring AC back to previous state and send ack to cloud to notify regarding this behaviour

## Slide 23
Key | Value | Type | Range
JsonPacketId | 5 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
Reconfiguration packet
Key | Value | Type | Range
JsonPacketId | 5 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
ErrorCode | 0 | Number | 0 - 6
Reconfiguration ack
Gateway
Cloud
1. Reconfiguration packet is sent from Cloud to Gateway
LTE
2. Gateway sends reconfiguration ack to cloud
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 5,
"MsgSeqNo": 1,
"GwySerNo": 2
}
Gateway Reconfiguration
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 5,
"MsgSeqNo": 1,
"GwySerNo": 2,
"ErrorCode": 0
}
Gateway reconfiguration is the process in which user can configure the gateway to use a different protocol from the one it was using before.

## Slide 24
Gateway
Reset MQTT configuration
LTE
Key | Value | Type | Range
JsonPacketId | 9 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 00001 | Number | 0 - 65535
MQTT configuration packet
Key | Value | Type | Range
JsonPacketId | 9 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 00001 | Number | 0 - 65535
Error Code | 0 | Number | 0 - 3
MQTT Configuration Ack
Json packet (Cloud -> Gateway)
{
"JsonPacketId" : 9,
"MsgSeqNo": 12,
"GwySerNo": "GWY00005",
}
Cloud
1. Reset MQTT configuration Json packet sent from Cloud to Gwy
2. Gwy sends back Reset MQTT configuration Ack
Json ack (Gateway -> Cloud)
{
"JsonPacketId" : 12,
"MsgSeqNo": 12,
"GwySerNo": "GWY00005",
"Errorcode": 0
}
Upon receiving this packet, the Gateway will enter MQTT configuration mode. User will be able to connect with the Gateway’s Wifi hotspot.
After connecting to Gateway’s Wifi, at the IP 192.168.1.1, Gateway MQTT configuration site will be loaded, wherein user can enter the MQTT parameter details and press ‘Submit’.
Gateway will fetch the values and try to establish MQTT connection. If successful, then it will exit MQTT configuration mode, if not, it will stay in the MQTT configuration mode

## Slide 25
Key | Value | Type | Range
JsonPacketId | 6 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
MacId | "b0:b2:1c:8f:a7:be" | String | 17 char long
Location | "1st Floor" | String | 20 char long
Provisioning packet
Key | Value | Type | Range
JsonPacketId | 6 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 1 | String | 4 Char long
Location | "1st Floor" | String | 20 char long
ErrorCode | 0 | Number | 0 - 6
Provisioning ack
Gateway
Cloud
Node
1. Provision packet is sent from cloud to gateway
2. Provision packet is sent from cloud to gateway
LTE
BLE
3a. If provision packet recvd from cloud has error, ack send back to cloud with error code
3b. Node sends provisioning ack to Gateway
4. Gateway send provisioning ack back to cloud
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 6,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"MacId": "b0:b2:1c:8f:a7:be",
"Location": "1st floor"
}
Node Provisioning
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 6,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 55,
"Location" : "1st floor",
"ErrorCode" : 0
}
Node provisioning is the process of adding a Node into the Mesh network.
Using the Mobile app, user will scan the QR code sticker placed on the Node device. The QR code contains all information related to the Node.

## Slide 26
Gateway
Cloud
Node
LTE
BLE
Node Configuration
1. Node sends configuration information to Gateway
2. Gateway sends configuration info of node to cloud
Key | Value | Type | Range
JsonPacketId | 7 | Number | 0 - 99
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 1 | String | 4 Char long
ErrorCode | 0 | Number | 0 - 6
Configuration status
Error code | Meaning
0 | Success
1 | Invalid GwySerNo
2 | Invalid NodeSerNo
3 | Invalid ElemAddr
4 | Invalid protocol
Error codes
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 7,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr" : 55,
"Errorcode" : 0,
}
Node Configuration is the process in which the node is set to use a specific protocol for controlling the Air conditioner.
A provisioned node will be waiting in configuration mode until configured.
When a supported AC remote button is pressed in front of the node’s receiver, the node will get configured to act as that AC remote.

## Slide 27
Key | Value | Type | Range
JsonPacketId | 8 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 1 | String | 4 Char long
UnProvisioning packet
Key | Value | Type | Range
JsonPacketId | 8 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 1 | String | 4 Char long
ErrorCode | 0 | Number | 0 - 6
UnProvisioning ack
Gateway
Cloud
Node
1. Unprovision packet is sent from cloud to gateway
2. Unprovision packet is sent from cloud to gateway
LTE
BLE
3a. If Unprovision packet received from cloud has error, ack send back to cloud with error code
3b. Node sends Unprovisioning ack to Gateway
4. Gateway send Unprovisioning ack back to cloud
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 8,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 55,
}
Node Unprovisioning
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 8,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 55,
"ErrorCode": 0
}
Node Unprovisioning is the process of removing a Node from the Mesh network.

## Slide 28
Gateway
Cloud
Node
LTE
BLE
Node AC Control
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 9,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 4,
"Power": 1,
"Mode": "Cool",
"Fan": 5,
"Temp": 25,
"SwingH": 1,
"SwingV": 1,
"OnTimer": 0,
"OffTimer": 0,
"Locking": 1
}
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 9,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 4,
"Power": 1,
"Mode": "Cool",
"Fan": 5,
"Temp": 25,
"SwingH": 1,
"SwingV": 1,
"OnTimer": 0,
"OffTimer": 0,
"Locking": 1,
"Errorcode": 0,
}
1. Control packet is sent from the cloud
3a. If control packet received from cloud is invalid, control ack is sent back to the cloud with respective error code.
2. Control packet is sent to the node after parsing is successful
3b. Node sends control ack to Gateway
4. Gateway send control ack back to cloud

## Slide 29
Key | Value | Type | Range
JsonPacketId | 9 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 – 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 55 | Number | 0 - 65535
Power | 1 = ON, 0 = OFF | Number | 0, 1
Mode | "Cool" | String | "Cool", "Hot", "Dry", "Auto", "Quiet"
Fan | 2 | Number | 0 – 4
Temperature | 25 | Number | 16 - 32
SwingH | 1 = ON, 0 = OFF | Number | 0, 1
SwingV | 1 = ON, 0 = OFF | Number | 0, 1
OnTimer | 4 | Number (Hrs) | 0 – 12
OffTimer | 5 | Number (Hrs) | 0 – 12
Locking | 1 = ON, 0 = OFF | Number | 1, 0
Control packet
Key | Value | Type | Range
JsonPacketId | 9 | Number | 0 – 99
MsgSeqNo | 1 | Number | 0 – 65535
GwySerNo | 1 | Number | 0 – 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 55 | String | 4 Char long
Power | 1 = ON, 0 = OFF | Number | 0, 1
Mode | "Cool" | String | "Cool", "Hot", "Dry", "Auto", "Quiet"
Fan | 2 | Number | 0 – 4
Temperature | 25 | Number | 16 - 32
SwingH | 1 = ON, 0 = OFF | Number | 0, 1
SwingV | 1 = ON, 0 = OFF | Number | 0, 1
OnTimer | 4 | Number (Hrs) | 0 – 12
OffTimer | 5 | Number (Hrs) | 0 – 12
Locking | 1 = ON, 0 = OFF | Number | 1, 0
ErrorCode | 0 | Number | 0 - 15
Control ack

## Slide 30
Gateway
Cloud
Node
LTE
BLE
Node AC Locking
1. Node detects that AC got controlled by its remote and Locking feature is enabled.
2. Gateway sends this information to cloud
Key | Value | Type | Range
JsonPacketId | 10 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 55 | Number | 0 – 65535
Locking status
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 10,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr":55
}
Node notifies the Gateway regarding this. After that sends the IR command to bring AC back to the state it was

## Slide 31
Key | Value | Type | Range
JsonPacketId | 6 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 55 | String | 4 Char long
Reconfiguration packet
Key | Value | Type | Range
JsonPacketId | 6 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 55 | String | 4 Char long
ErrorCode | 0 | Number | 0 - 6
Reconfiguration ack
Gateway
Cloud
Node
1. Reconfiguration packet is sent from Cloud to Gateway
2. Reconfiguration packet is sent from cloud to gateway.
LTE
BLE
3a. If reconfiguratoin packet received from cloud has error, ack sent back to cloud with error code
3b. Node sends ack that it has entered configuration mode.
4. Gateway sends reconfiguration ack to cloud
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 11,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 55,
}
Node Reconfiguration
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 11,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 55,
"ErrorCode": 0,
}
Node enters configuration mode.
Node reconfiguration is the process in user can configure the node to use a different protocol from the one it was using before.
Alternatively, the User button can be pressed twice quickly to put the Node into configuration mode

## Slide 32
Mobile
Cloud
Gateway
Node
AC
(1)
User scans the QR code on the Gwy device from the mobile app
(1)
Cloud sends the Gateway Registration packet to the Specific Gwy
(2)
(3)
Gwy sends back ACK to cloud with appropriate Error code
(4)
User gets notified about the Registration status based on Error code

## Slide 33
Mobile
Cloud
Gateway
Node
AC
(1)
(1)
While Gwy is in AC Remote configuration mode, user presses AC remote in front of the IR receiver. Gwy sends Configuration ACK to cloud
(2)
User gets notified about the Configuration status based on Error code

## Slide 34
Mobile
Cloud
Gateway
Node
AC
(1)
User presses “Unregister” button from the app
(1)
Cloud sends the Gateway Unregistration packet to the Specific Gwy
(2)
(3)
Gwy sends back ACK to cloud with appropriate Error code
(4)
User gets notified about the Unregistration status based on Error code

## Slide 35
Mobile
Cloud
Gateway
Node
AC
(1)
User configures AC control parameters and presses “Gwy AC Control” button from the app
(1)
Cloud sends the Gateway AC Control packet to the Specific Gwy
(2)
(3)
Gwy sends back ACK to cloud with appropriate Error code
(4)
User gets notified about the AC Control status based on Error code

## Slide 36
Mobile
Cloud
Gateway
Node
AC
(1)
(1)
Gwy sends AC manual control ACK to Cloud
(2)
User is made aware about the manual control of AC

## Slide 37
Mobile
Cloud
Gateway
Node
AC
(1)
User presses “Gwy AC Remote Reconfigure” button from the app
(1)
Cloud sends the Gateway AC Remote Reconfiguration packet to the Specific Gwy
(2)
(3)
Gwy sends back ACK to cloud with appropriate Error code
(4)
User gets notified about the Reconfiguration status based on Error code

## Slide 38
Mobile
Cloud
Gateway
Node
AC
(1)
(1)
Gwy sends Heartbeat Ack to Cloud
(2)
Mobile app receives the Heartbeat ACK and sets the Gwy alive status to True

## Slide 39
Mobile
Cloud
Gateway
Node
AC
(1)
User presses “Gwy Heartbeat publish configuration” button from mobile app.
(1)
Cloud sends the Gateway Heartbeat Publish Configuration packet to the Specific Gwy
(2)
(3)
Gwy sends back ACK to cloud with appropriate Error code
(4)
User gets notified about the Gwy Heartbeat publish configuration based on Error code

## Slide 40
Mobile
Cloud
Gateway
Node
AC
(1)
User presses “Gwy Debug Info Packet” button from mobile app.
(1)
Cloud sends the Gateway Debug Info packet to the Specific Gwy
(2)
(3)
Gwy sends back ACK to cloud with appropriate Error code
(4)
User gets Gwy Debug information from the ACK

## Slide 41
Mobile
Cloud
Gateway
Node
AC
(1)
(1)
Gwy sends Heartbeat Ack to Cloud
(2)
Mobile app updates the alive status for the Gwy

## Slide 42
Mobile
Cloud
Gateway
Node
AC
(1)
User presses “Reset MQTT” button from mobile app.
(1)
Cloud sends the Gateway Reset MQTT packet to the Specific Gwy
(2)
(3)
Gwy sends back ACK to cloud with appropriate Error code
(4)
User gets notified about the AC Control status based on Error code

## Slide 43
Mobile
Cloud
Gateway
Node
AC
(1)
User presses “Teaching mode” button from the app
(1)
Cloud sends the Gateway Teaching mode packet to the Specific Gwy
(2)
(3)
Gwy sends back ACK to cloud with appropriate Error code
(4)
User gets notified if the Gwy has entered teaching mode based on Error code

## Slide 44
Mobile
Cloud
Gateway
Node
AC
(1)
(1)
Gwy sends Teaching Mode End ack to cloud
(2)
User is notifed that the Gwy has exited teaching mode based on error code

## Slide 46
Mobile
Cloud
Gateway
Node
AC
(1)
User scans the QR code on the Node device
(1)
Cloud sends the Node provisioning packet to the Specific Gwy
(2)
(5)
Gwy sends back ACK to cloud with appropriate Error code
(6)
User gets notified about the Node provisioning status based on Error code
Gateway tries provisioning the Node into the BLE Mesh network.
(3)
(4)
Node sends back Ack to Gwy reg. the provisioning status

## Slide 47
Mobile
Cloud
Gateway
Node
AC
(1)
(2)
Gwy sends back Node configuration ack to cloud with appropriate Error code
(3)
User gets notified about the Node provisioning status based on Error code
(1)
When Node is in configuration mode, user presses AC remote button in front of the IR recevier in the node. Node sends configuration ack to Gwy

## Slide 48
Mobile
Cloud
Gateway
Node
AC
(1)
User presses “Node unprovision” button from the mobile app
(1)
Cloud sends the Node Unprovisioning packet to the Specific Gwy
(2)
(4)
Gwy sends back ACK to cloud with appropriate Error code
(5)
User gets notified about the Node Unprovisioning status based on Error code
Gateway tries Unprovisioning the Node into the BLE Mesh network.
(3)

## Slide 49
Mobile
Cloud
Gateway
Node
AC
(1)
User presses “Node AC Control” button from the mobile app
(1)
Cloud sends the Node AC Control packet to the Specific Gwy
(2)
(5)
Gwy sends back ACK to cloud with appropriate Error code
(6)
User gets notified about the Node provisioning status based on Error code
Gateway sends the Node AC Control packet to the Node
(3)
(4)
Node sends back Ack to Gwy reg. the AC Control status

## Slide 50
Mobile
Cloud
Gateway
Node
AC
(1)
(2)
Gwy sends Node AC manual ack to cloud
(3)
User gets notified about the manual control status of a node controlled AC
(1)
Node sends AC manual control Ack to Gwy

## Slide 51
Mobile
Cloud
Gateway
Node
AC
(1)
User presses “Node AC Remote reconfiguration” button from the mobile app
(1)
Cloud sends the Node AC Remote Reconfiguration packet to the Specific Gwy
(2)
(5)
Gwy sends back ACK to cloud with appropriate Error code
(6)
User gets notified if the node entered AC remote reconfiguration mode or not based on the error code.
Gateway sends the Node AC Remote reconfiguration packet to the Node
(3)
(4)
Node enters AC Remote configuration mode and sends back Ack to Gwy.

## Slide 52
Mobile
Cloud
Gateway
Node
AC
(1)
(2)
Gwy sends Node Temperature data ack to cloud
(3)
User gets notified about the Node Locking status based on Error code
(1)
Node sends Temperature data Ack to Gwy

## Slide 53
Mobile
Cloud
Gateway
Node
AC
(1)
User presses “Node Heartbeat publish configuration” button from the mobile app
(1)
Cloud sends the Node Heartbeat Publish configuration packet to the Specific Gwy
(2)
(5)
Gwy sends back ACK to cloud with appropriate Error code
(6)
User gets notified about the Node Heartbeat Publish configuration status based on Error code
Gateway sends the Node Heartbeat Publish configuration packet to the Node
(3)
(4)
Node sends back Heartbeat Publish configuration ack to Gwy

## Slide 54
Mobile
Cloud
Gateway
Node
AC
(1)
(2)
Gwy sends Node Heartbeat ack to cloud
(3)
User gets notified about the Node alive status.
(1)
Node sends Heartbeat Ack to Gwy

## Slide 55
Mobile
Cloud
Gateway
Node
AC
(1)
User presses “Heartbeat configuration” button from the mobile app
(1)
Cloud sends the Heartbeat configuration packet to the all Gwys
(2)
(5)
Gwy sends back Gwy Heartbeat configuration ack and Node Heartbeat configuration ack to cloud
(6)
User gets notified about the Heartbeat configuration status based on Error code
Gateways configure their Heartbeat intervals and send the packet to Nodes
(3)
(4)
Nodes configure their Heartbeat interval and send the Ack to Gateway

## Slide 56
Mobile
Cloud
Gateway
Node
AC
(1)
User pressed "Teaching mode start" button for Node from mobile app
(1)
Cloud sends the Node Teaching Mode Start Packet to the Specific Gwy
(2)
(5)
Gwy sends back Node Teaching Mode Start ACK to cloud with appropriate Error code
(6)
User gets notified if the Node has entered teaching mode or not based on error code
Gateway sends the Node Teaching Mode Start Packet to specific Node.
(3)
(4)
Node sends back Ack to Gwy reg. If it entered teaching mode

## Slide 57
Mobile
Cloud
Gateway
Node
AC
(1)
(2)
Gwy sends Node Teaching Mode end ACK to Cloud
(3)
User gets notified if the Node has exited teaching mode or not based on error code
(1)
Node sends Node Teaching mode end ACK to Gwy

## Slide 58
Mobile
Cloud
Gateway
Node
AC
(1)
Sending “Node Debug Info Packet”
(1)
Cloud sends the Node Debug info packet to the Specific Gwy
(2)
(5)
Gwy sends back Node Debug info ACK to cloud
(6)
Node debug info packet is received and can be used for debugging
Gateway sends the Node Debug info packet to specific Node.
(3)
(4)
Node sends back the Debug info ACK back to Gwy