## Slide 1: BLE Mesh based IR AC Controller Software Design Document-Cloud & Gateway
Prepared by:-Kulasekaran
12-Feb-2024

## Slide 2
Reference
JsonPacketID | Packet | Description
0 | Gateway Registration | Json packet containing information about Gateway to add it into the mesh network
1 | Gateway Configuration | Json ack to cloud containing information about a Gateway configuration status
2 | Gateway Unregistration | Json packet containing information about Gateway to remove it from the mesh network
3 | Gateway AC Control | Json packet containing all AC setting information for controlling AC using a Gateway
4 | Gateway AC Locking | Json ack to cloud containing information about locking from Gateway
5 | Gateway Reconfiguration | Json packet which will set gateway to enter configuration mode
6 | Node Provisioning | Json packet containing information about node to add into the mesh network
7 | Node Configuration | Json ack to cloud containing information about a node configuration status
8 | Node Unprovisioning | Json packet containing information about node to remove it from the mesh network
9 | Node AC Control | Json packet contatining all AC setting information for controlling AC using a node
10 | Node AC Locking | Json ack to cloud containing information about locking from Node
11 | Node Reconfiguration | Json packet which will set Node to enter configuration mode

## Slide 3
PROCESS FLOW DIAGRAM
Cloud
Gateway
Node
User scans QR code on the Gateway device with mobile app. Registration packet with Gateway details gets sent.
Registration packet is received. Gateway is added into network
User gets notified about the registration status.
Registration ack is sent to cloud
Gateway Registration
Configuration status ack is sent to cloud
Users gets notified regarding the configuration status of the Gateway.
Gateway Configuration
Registered gateway will listen for supported AC remotes’s button press.
Gateway Unregistration
User presses unregister button in the Mobile app for specific Gateway device
Unregistration packet is received. Gateway is removed from network
User gets notified about the Unregistration status.
Unregistration ack is sent to cloud

## Slide 4
PROCESS FLOW DIAGRAM
Cloud
Gateway
Node
User inputs AC control setting in the app for a particular Node and presses the control button. Control packet gets sent from cloud
Control packet is received and validated
Control ack gets sent back to the cloud
User gets notified regarding the control status.
Locking status ack is sent to the cloud and last IR command is sent to maintain the AC state
User gets notified regarding that a particular AC was controlled using remote and t
Users presses reconfigure button for a Node/Gateway. Reconfiguration packet is sent
Reconfiguration packet received and validated
Reconfiguration ack is passed to Cloud
User gets notified regarding the reconfiguration status
Gateway AC Control
Gateway AC Locking
Gateway Reconfiguration
Locking is enabled. Gateway detected that AC was controlled using remote.

## Slide 5
PROCESS FLOW DIAGRAM
Cloud
Gateway
Node
User scans QR code on a Node device with mobile app. Provisioning packet with Node details gets sent.
Provisioning packet is received and verified. If valid, it is sent to the particular node.
Provisioning packet is received. Node gets provisioned and enters configuration mode.
Provisioning ack is sent to gatewa. (Provisioned node will wait in config mode until configured)
Received provisioning ack from Node and is sent to cloud
Users gets notified regarding the Provisioning status.
While node is waiting in Config mde, a supported AC remote’s button is pressed in front of Node’s receiver
Node detects the IR protocol and gets configured. Sends this information to Gateway
Configuration status information received from Node and sent to cloud.
Users gets notified regarding the configuration status of the node.
Node Provisioning
Node Configuration
User presses unprovision button for specific node on the mobile app
Unprovisioning packet is received and verified. If valid, it is sent to the particular node.
Unprovisioning packet is received. Node gets removed from the network
Unprovisioning ack is sent to gateway
Received Unprovisioning ack from Node and is sent to cloud
Users gets notified regarding the Unprovisioning status.
Node Unprovisioning

## Slide 6
PROCESS FLOW DIAGRAM
Cloud
Gateway
Node
User inputs AC control setting in the app for a particular Node and presses the control button. Control packet gets sent from cloud
Control packet is received and if valid, it is sent to Node.
Node receives the control packet and controls the AC. Sends back Ack to the Gateway
If control packet was invalid, ack with error code gets sent to cloud
User gets notified regarding the control status.
If invalid
Locking is enabled. Node detected that AC was controlled using remote.
Sends this information to Gateway. Also sends back previous IR command to maintain the AC’s locked state.
Gateway receives the locking status info from Node and sends it to cloud
User gets notified regarding that a particular AC was controlled using remote and t
Users presses reconfigure button for a Node/Gateway. Reconfiguration packet is sent
Reconfiguration packet received and if valid, it is sent to Node.
Reconfiguration packet is received. Node enters Configuration mode.
Reconfiguraion ack is sent.
Reconfiguration ack is received. Ack is passed to Cloud
User gets notified regarding the reconfiguration status
Node AC Control
Node Locking
Node Reconfiguration

## Slide 7
Gateway
Gateway Registration
LTE
Key | Value | Type | Range
JsonPacketId | 0 | Number | 0 - 99
MsgSeqNo | 12 | Number | 0 - 65535
GwySerNo | 00001 | Number | 0 - 65535
Location | "1st floor" | String | 20 char long
Registration Packet
Key | Value | Type | Range
JsonPacketId | 0 | Number | 0 - 99
MsgSeqNo | 12 | Number | 0 - 65535
GwySerNo | 00001 | Number | 0 - 65535
Location | "1st floor" | String | 20 char long
Error Code | 0 | Number | 0 - 3
Registration Packet Ack
Error code | Meaning
0 | Success
1 | Invalid MsgSeqNo
2 | Invalid GwySerNo
3 | Invalid Location
4 | Invalid JsonPacketId
Error codes
Json packet (Cloud -> Gateway)
{
"JsonPacketId" : 0,
"msgSeqNo": 12,
"gatewaySerNo": "GWY00005",
"location": "ABCD Showroom“
}
Cloud
1. Registration Json packet sent from Cloud to Gwy
2. Gwy sends back registration Ack
Json ack (Gateway -> Cloud)
{
"JsonPacketId" : 0,
"msgSeqNo": 12,
"gatewaySerNo": "GWY00005",
"location": "ABCD Showroom",
"Errorcode": 0
}
Gateway registration is the process of adding a gateway into the Mesh network.
Using the Mobile app, user will scan the QR code sticker placed on the Gateway device. The QR code contains all information related to the Gateway.

## Slide 8
Gateway
Cloud
LTE
Gateway Configuration
1. Gateway sends configuration status ack to cloud
Key | Value | Type | Range
JsonPacketId | 1 | Number | 0 - 99
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ErrorCode | 0 | Number | 0 - 6
Configuration status
Error code | Meaning
0 | Success
1 | Invalid GwySerNo
2 | Invalid NodeSerNo
3 | Invalid protocol
Error codes
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
“Errorcode” : 0
}
Gateway Configuration is the process in which the node is set to use a specific protocol for controlling the Air conditioner.
A registered unconfigured gateway will be waiting in configuration mode until configured.
When a supported AC remote button is pressed in front of the Gateway’s receiver, the gateway will get configured to act as that AC remote.

## Slide 9
Gateway Unregistration
Gateway
Key | Value | Type | Range
jsonPacketId | 2 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 00001 | Number | 0 - 65535
Location | "1st floor" | String | 20 char long
Un-Registration Packet
Key | Value | Type | Range
JsonPacketId | 2 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 00001 | Number | 0 - 65535
Location | "1st floor" | String | 20 char long
Error Code | 0 | Number | 0 - 3
Un-Registration Packet Ack
Error code | Meaning
0 | Success
1 | Invalid MsgSeqNo
2 | Invalid GwySerNo
3 | Invalid Location
4 | Invalid JsonPacketId
Error codes
Cloud
1. Unregistration Json packet sent from Cloud to Gwy
2. Gwy sends back UnRegistration Ack back to cloud
Json packet (Cloud -> Gateway)
{
"JsonPacketId" : 2,
"msgSeqNo": 12,
"gatewaySerNo": "GWY00005",
"location": "ABCD Showroom“
}
LTE
Json ack (Cloud -> Gateway)
{
"JsonPacketId" : 2,
"msgSeqNo": 12,
"gatewaySerNo": "GWY00005",
"location": "ABCD Showroom",
"Errorcode": 0,
}
Gateway Unregistration is the process of removing a gateway from the Mesh network.

## Slide 10
Gateway
Cloud
LTE
Gateway AC Control
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 3,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
“Power": 1,
“Mode": "Cool",
“Fan": 5,
“Temp": 25,
“SwingH": 1,
“SwingV": 1,
"OnTimer": 0,
"OffTimer": 0,
"Locking": 1
}
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 3,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
“Power": 1,
“Mode": "Cool",
“Fan": 5,
“Temp": 25,
“SwingH": 1,
“SwingV": 1,
"OnTimer": 0,
"OffTimer": 0,
"Locking": 1,
“Errorcode”: 0,
}
1. Control packet is sent from the cloud
2. Gateway sends control ack back to cloud

## Slide 11
Key | Value | Type | Range
JsonPacketId | 3 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 – 65535
GwySerNo | 1 | Number | 0 – 65535
Power | 1 = ON, 0 = OFF | Number | 0, 1
Mode | "Cool" | String | "Cool", "Hot", "Dry", "Auto", "Quiet"
Fan | 2 | Number | 0 – 4
Temperature | 25 | Number | 16 - 32
SwingH | 1 = ON, 0 = OFF | Number | 0, 1
SwingV | 1 = ON, 0 = OFF | Number | 0, 1
OnTimer | 4 | Number | 0 – 12
OffTimer | 5 | Number | 0 – 12
Locking | 1 = ON, 0 = OFF | Number | 1, 0
Control packet
Key | Value | Type | Range
JsonPacketId | 3 | Number | 0 – 99
MsgSeqNo | 1 | Number | 0 – 65535
GwySerNo | 1 | Number | 0 – 65535
Power | 1 = ON, 0 = OFF | Number | 0, 1
Mode | "Cool" | String | "Cool", "Hot", "Dry", "Auto", "Quiet"
Fan | 2 | Number | 0 – 4
Temperature | 25 | Number | 16 - 32
SwingH | 1 = ON, 0 = OFF | Number | 0, 1
SwingV | 1 = ON, 0 = OFF | Number | 0, 1
OnTimer | 4 | Number | 0 – 12
OffTimer | 5 | Number | 0 – 12
Locking | 1 = ON, 0 = OFF | Number | 1, 0
ErrorCode | 0 | Number | 0 - 15
Control ack
Error code | Meaning
0 | Success
1 | Invalid GwySerNo
4 | Invalid Power
5 | Invalid Mode
6 | Invalid Fan
7 | Invalid Temperature
8 | Invalid SwingH
9 | Invalid SwingV
10 | Invalid OnTimer
11 | Invalid OffTimer
12 | Invalid Locking
Error codes

## Slide 12
Gateway
Cloud
LTE
Gateway AC Locking
1. Gateway detects that AC got controlled by its remote and Locking feature is enabled.
Key | Value | Type | Range
JsonPacketId | 4 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 – 65535
GwySerNo | 1 | Number | 0 – 65535
NodeSerNo | 1 | Number | 0 – 65535
Locking status
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 4,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
}
Gateway sends back previous IR command to bring AC back to previous state and send ack to cloud to notify regarding this behaviour

## Slide 13
Key | Value | Type | Range
JsonPacketId | 5 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
Reconfiguration packet
Key | Value | Type | Range
JsonPacketId | 5 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ErrorCode | 0 | Number | 0 - 6
Reconfiguration ack
Error code | Meaning
0 | Success
1 | Invalid MsgSeqNo
2 | Invalid GwySerNo
3 | Invalid NodeSerNo
4 | Time out
Error codes
Gateway
Cloud
1. Reconfiguration packet is sent from Cloud to Gateway
LTE
2. Gateway sends reconfiguration ack to cloud
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 5,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 5a,
}
Gateway Reconfiguration
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 5,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 5a,
"ErrorCode": 0,
}
Gateway reconfiguration is the process in which user can configure the gateway to use a different protocol from the one it was using before.

## Slide 14
Key | Value | Type | Range
JsonPacketId | 6 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
MacId | "b0:b2:1c:8f:a7:be" | String | 17 char long
Location | “1st Floor” | String | 20 char long
Provisioning packet
Key | Value | Type | Range
JsonPacketId | 6 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 1 | Number | 0 – 65535
Location | “1st Floor” | String | 20 char long
ErrorCode | 0 | Number | 0 - 6
Provisioning ack
Error code | Meaning
0 | Success
1 | Invalid MsgSeqNo
2 | Invalid GwySerNo
3 | Invalid NodeSerNo
4 | Invalid MacID
5 | Time out
6 | Already Provisioned
Error codes
Gateway
Cloud
Node
1. Provision packet is sent from cloud to gateway
2. Provision packet is sent from cloud to gateway
LTE
BLE
3a. If provision packet recvd from cloud has error, ack send back to cloud with error code
3b. Node sends provisioning ack to Gateway
4. Gateway send provisioning ack back to cloud
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 6,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"MacId": "b0:b2:1c:8f:a7:be“,
“Location”: “1st floor”
}
Node Provisioning
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 6,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 5a,
“Location” : “1st floor”,
“ErrorCode” : 0
}
Node provisioning is the process of adding a Node into the Mesh network.
Using the Mobile app, user will scan the QR code sticker placed on the Node device. The QR code contains all information related to the Node.

## Slide 15
Gateway
Cloud
Node
LTE
BLE
Node Configuration
1. Node sends configuration information to Gateway
2. Gateway sends configuration info of node to cloud
Key | Value | Type | Range
JsonPacketId | 7 | Number | 0 - 99
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 1 | Number | 0 – 65535
ErrorCode | 0 | Number | 0 - 6
Configuration status
Error code | Meaning
0 | Success
1 | Invalid GwySerNo
2 | Invalid NodeSerNo
3 | Invalid ElemAddr
4 | Invalid protocol
Error codes
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 7,
"GwySerNo": 2,
"NodeSerNo": 3,
“ElementAddr” : 5a,
“Errorcode” : 0,
}
Node Configuration is the process in which the node is set to use a specific protocol for controlling the Air conditioner.
A provisioned node will be waiting in configuration mode until configured.
When a supported AC remote button is pressed in front of the node’s receiver, the node will get configured to act as that AC remote.

## Slide 16
Key | Value | Type | Range
JsonPacketId | 8 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 1 | Number | 0 – 65535
UnProvisioning packet
Key | Value | Type | Range
JsonPacketId | 8 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 1 | Number | 0 – 65535
ErrorCode | 0 | Number | 0 - 6
UnProvisioning ack
Error code | Meaning
0 | Success
1 | Invalid MsgSeqNo
2 | Invalid GwySerNo
3 | Invalid NodeSerNo
4 | Invalid ElemAddr
5 | Time out
Error codes
Gateway
Cloud
Node
1. Unprovision packet is sent from cloud to gateway
2. UnProvision packet is sent from cloud to gateway
LTE
BLE
3a. If Unprovision packet received from cloud has error, ack send back to cloud with error code
3b. Node sends Unprovisioning ack to Gateway
4. Gateway send Unprovisioning ack back to cloud
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 8,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 5a,
}
Node Unprovisioning
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 8,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 5a,
"ErrorCode": 0
}
Node Unprovisioning is the process of removing a Node from the Mesh network.

## Slide 17
Gateway
Cloud
Node
LTE
BLE
Node AC Control
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 9,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 4,
“Power": 1,
“Mode": "Cool",
“Fan": 5,
“Temp": 25,
“SwingH": 1,
“SwingV": 1,
"OnTimer": 0,
"OffTimer": 0,
"Locking": 1
}
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 9,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 4,
“Power": 1,
“Mode": "Cool",
“Fan": 5,
“Temp": 25,
“SwingH": 1,
“SwingV": 1,
"OnTimer": 0,
"OffTimer": 0,
"Locking": 1,
“Errorcode”: 0,
}
1. Control packet is sent from the cloud
3a. If control packet received from cloud is invalid, control ack is sent back to the cloud with respective error code.
2. Control packet is sent to the node after parsing is successful
3b. Node sends control ack to Gateway
4. Gateway send control ack back to cloud

## Slide 18
Key | Value | Type | Range
JsonPacketId | 9 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 – 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 5a | Number | 0 – 65535
Power | 1 = ON, 0 = OFF | Number | 0, 1
Mode | "Cool" | String | "Cool", "Hot", "Dry", "Auto", "Quiet"
Fan | 2 | Number | 0 – 4
Temperature | 25 | Number | 16 - 32
SwingH | 1 = ON, 0 = OFF | Number | 0, 1
SwingV | 1 = ON, 0 = OFF | Number | 0, 1
OnTimer | 4 | Number | 0 – 12
OffTimer | 5 | Number | 0 – 12
Locking | 1 = ON, 0 = OFF | Number | 1, 0
Control packet
Key | Value | Type | Range
JsonPacketId | 9 | Number | 0 – 99
MsgSeqNo | 1 | Number | 0 – 65535
GwySerNo | 1 | Number | 0 – 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 5a | Number | 0 – 65535
Power | 1 = ON, 0 = OFF | Number | 0, 1
Mode | "Cool" | String | "Cool", "Hot", "Dry", "Auto", "Quiet"
Fan | 2 | Number | 0 – 4
Temperature | 25 | Number | 16 - 32
SwingH | 1 = ON, 0 = OFF | Number | 0, 1
SwingV | 1 = ON, 0 = OFF | Number | 0, 1
OnTimer | 4 | Number | 0 – 12
OffTimer | 5 | Number | 0 – 12
Locking | 1 = ON, 0 = OFF | Number | 1, 0
ErrorCode | 0 | Number | 0 - 15
Control ack
Error code | Meaning
0 | Success
1 | Invalid GwySerNo
2 | Invalid NodeSerNo
3 | NodeSerNo – ElementAddr mismatch
4 | Invalid ElementAddr
5 | Invalid Power
6 | Invalid Mode
7 | Invalid Fan
8 | Invalid Temperature
9 | Invalid SwingH
10 | Invalid SwingV
11 | Invalid OnTimer
12 | Invalid OffTimer
13 | Invalid Locking
Error codes

## Slide 19
Gateway
Cloud
Node
LTE
BLE
Node AC Locking
1. Node detects that AC got controlled by its remote and Locking feature is enabled.
2. Gateway sends this information to cloud
Key | Value | Type | Range
JsonPacketId | 10 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 1 | Number | 0 – 65535
Locking status
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 10,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
“ElementAddr”:5a
}
Node notifies the Gateway regarding this. After that sends the IR command to bring AC back to the state it was

## Slide 20
Key | Value | Type | Range
JsonPacketId | 6 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 5a | Number | 0 – 65535
Reconfiguration packet
Key | Value | Type | Range
JsonPacketId | 6 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65535
GwySerNo | 1 | Number | 0 - 65535
NodeSerNo | 1 | Number | 0 – 65535
ElementAddr | 5a | Number | 0 – 65535
ErrorCode | 0 | Number | 0 - 6
Reconfiguration ack
Error code | Meaning
0 | Success
1 | Invalid MsgSeqNo
2 | Invalid GwySerNo
3 | Invalid NodeSerNo
4 | Invalid ElemAddr
5 | Time out
Error codes
Gateway
Cloud
Node
1. Reconfiguration packet is sent from Cloud to Gateway
2. Reconfiguration packet is sent from cloud to gateway.
LTE
BLE
3a. If reconfiguratoin packet received from cloud has error, ack sent back to cloud with error code
3b. Node sends ack that it has entered configuration mode.
4. Gateway sends reconfiguration ack to cloud
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 11,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 5a,
}
Node Reconfiguration
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 11,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 5a,
"ErrorCode": 0,
}
Node enters configuration mode.
Node reconfiguration is the process in user can configure the node to use a different protocol from the one it was using before.