## Slide 2
PROCESS FLOW DIAGRAM
Cloud
Gateway
Node
User scans QR code on the Gateway device with mobile app. Registration packet with Gateway details gets sent.
Registration packet is received. Gateway is added into network
User scans QR code on a Node device with mobile app. Provisioning packet with Node details gets sent.
Provisioning packet is received and verified. If valid, it is sent to the particular node.
Provisioning packet is received. Node gets provisioned and enters configuration mode.
Provisioning ack is sent to gatewa. (Provisioned node will wait in config mode until configured)
Received provisioning ack from Node and is sent to cloud
Users gets notified regarding the Provisioning status.
User gets notified about the registration status.
Registration ack is sent to cloud
While node is waiting in Config mde, a supported AC remote’s button is pressed in front of Node’s receiver
Node detects the IR protocol and gets configured. Sends this information to Gateway
Configuration status information received from Node and sent to cloud.
Users gets notified regarding the configuration status of the node.
Gateway Registration
Node Provisioning
Node Configuration

## Slide 3
PROCESS FLOW DIAGRAM
Cloud
Gateway
Node
User inputs AC control setting in the app for a particular Node and presses the control button. Control packet gets sent from cloud
Control packet is received and if valid, it is sent to Node.
Node receives the control packet and controls the AC. Sends back Ack to the Gateway
If control packet was invalid, ack with error code gets sent to cloud
User gets notified regarding the control status.
If invalid
Locking is enabled. Node detected that AC was controlled using remote.
Sends this information to Gateway. Also sends back previous IR command to maintain the AC’s locked state.
Gateway receives the locking status info from Node and sends it to cloud
User gets notified regarding that a particular AC was controlled using remote and t
Users presses reconfigure button for a node. Reconfiguration packet is sent
Reconfiguration packet received and if valid, it is sent to Node.
Reconfiguration packet is received. Node enters Configuration mode.
Reconfiguraion ack is sent.
Reconfiguration ack is received. Ack is passed to Cloud
User gets notified regarding the reconfiguration status
Control
Locking
Node Reconfiguration

## Slide 4
Gateway
Gateway Registration
LTE
Key | Value | Type | Range
JsonPacketId | 0 | Number | 0 - 99
MsgSeqNo | 12 | Number | 0 - 65536
GwySerNo | 00001 | Number | 0 - 65536
Location | "1st floor" | String | 20 char long
Timestamp | “Timestamp": "2022-07-19t12:01:36z” | String | 20 char long
Registration Packet
Key | Value | Type | Range
JsonPacketId | 0 | Number | 0 - 99
MsgSeqNo | 12 | Number | 0 - 65536
GwySerNo | 00001 | Number | 0 - 65536
Location | "1st floor" | String | 20 char long
Error Code | 0 | Number | 0 - 3
Registration Packet Ack
Error code | Meaning
0 | Success
1 | Invalid MsgSeqNo
2 | Invalid GwySerNo
3 | Invalid Location
4 | Invalid JsonPacketId
Error codes
Json packet (Cloud -> Gateway)
{
"JsonPacketId" : 0,
"msgSeqNo": 12,
"gatewaySerNo": "GWY00005",
"location": "ABCD Showroom“,
“Timestamp": "2022-07-19t12:01:36z”
}
Cloud
1. Registration Json packet sent from Cloud to Gwy
2. Gwy sends back registration Ack
Json ack (Gateway -> Cloud)
{
"JsonPacketId" : 0,
"msgSeqNo": 12,
"gatewaySerNo": "GWY00005",
"location": "ABCD Showroom",
"Errorcode": 0
“Timestamp” : “2022-07-19t12:01:36z”
}
Gateway registration is the process of adding a gateway into the Mesh network.
Using the Mobile app, user will scan the QR code sticker placed on the Gateway device. The QR code contains all information related to the Gateway.

## Slide 5
Gateway Unregistration
Gateway
Key | Value | Type | Range
jsonPacketId | 1 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65536
GwySerNo | 00001 | Number | 0 - 65536
Location | "1st floor" | String | 20 char long
Un-Registration Packet
Key | Value | Type | Range
JsonPacketId | 1 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65536
GwySerNo | 00001 | Number | 0 - 65536
Location | "1st floor" | String | 20 char long
Error Code | 0 | Number | 0 - 3
Un-Registration Packet Ack
Error code | Meaning
0 | Success
1 | Invalid MsgSeqNo
2 | Invalid GwySerNo
3 | Invalid Location
4 | Invalid JsonPacketId
Error codes
Cloud
1. Unregistration Json packet sent from Cloud to Gwy
2. Gwy sends back UnRegistration Ack back to cloud
Json packet (Cloud -> Gateway)
{
"JsonPacketId" : 1,
"msgSeqNo": 12,
"gatewaySerNo": "GWY00005",
"location": "ABCD Showroom“
“Timestamp": "2022-07-19t12:01:36z”
}
LTE
Json ack (Cloud -> Gateway)
{
"JsonPacketId" : 1,
"msgSeqNo": 12,
"gatewaySerNo": "GWY00005",
"location": "ABCD Showroom",
"Errorcode": 0,
"Timestamp": "2022-07-19t12:01:36z"
}
Gateway Unregistration is the process of removing a gateway from the Mesh network.

## Slide 6
Key | Value | Type | Range
JsonPacketId | 2 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65536
GwySerNo | 1 | Number | 0 - 65536
NodeSerNo | 1 | Number | 0 – 65536
MacId | "b0:b2:1c:8f:a7:be" | String | 17 char long
Timestamp | "2022-07-19t12:01:36z " | String | 20 char long
Provisioning packet
Key | Value | Type | Range
JsonPacketId | 2 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65536
GwySerNo | 1 | Number | 0 - 65536
NodeSerNo | 1 | Number | 0 – 65536
ElementAddr | 1 | Number | 0 – 65536
ErrorCode | 0 | Number | 0 - 6
Timestamp | "2022-07-19t12:01:36z " | String | 20 char long
Provisioning ack
Error code | Meaning
0 | Success
1 | Invalid MsgSeqNo
2 | Invalid GwySerNo
3 | Invalid NodeSerNo
4 | Invalid MacID
5 | Time out
6 | Already Provisioned
Error codes
Gateway
Cloud
Node
1. Provision packet is sent from cloud to gateway
2. Provision packet is sent from cloud to gateway
LTE
BLE
3a. If provision packet recvd from cloud has error, ack send back to cloud with error code
3b. Node sends provisioning ack to Gateway
4. Gateway send provisioning ack back to cloud
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 2,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"MacId": "b0:b2:1c:8f:a7:be",
"Timestamp": "2022-07-19t12:01:36z"
}
Node Provisioning
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 2,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 5a,
“ErrorCode” : 0,
"Timestamp": "2022-07-19t12:01:36z"
}
Node provisioning is the process of adding a Node into the Mesh network.
Using the Mobile app, user will scan the QR code sticker placed on the Node device. The QR code contains all information related to the Node.

## Slide 7
Key | Value | Type | Range
JsonPacketId | 3 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65536
GwySerNo | 1 | Number | 0 - 65536
NodeSerNo | 1 | Number | 0 – 65536
ElementAddr | 1 | Number | 0 – 65536
Timestamp | "2022-07-19t12:01:36z " | String | 20 char long
UnProvisioning packet
Key | Value | Type | Range
JsonPacketId | 3 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65536
GwySerNo | 1 | Number | 0 - 65536
NodeSerNo | 1 | Number | 0 – 65536
ElementAddr | 1 | Number | 0 – 65536
ErrorCode | 0 | Number | 0 - 6
Timestamp | "2022-07-19t12:01:36z " | String | 20 char long
UnProvisioning ack
Error code | Meaning
0 | Success
1 | Invalid MsgSeqNo
2 | Invalid GwySerNo
3 | Invalid NodeSerNo
4 | Invalid ElemAddr
5 | Time out
6 | Already Provisioned
Error codes
Gateway
Cloud
Node
1. Unprovision packet is sent from cloud to gateway
2. UnProvision packet is sent from cloud to gateway
LTE
BLE
3a. If Unprovision packet received from cloud has error, ack send back to cloud with error code
3b. Node sends Unprovisioning ack to Gateway
4. Gateway send Unprovisioning ack back to cloud
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 3,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 5a,
"Timestamp": "2022-07-19t12:01:36z"
}
Node Unprovisioning
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 3,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 5a,
"ErrorCode": 0,
"Timestamp": "2022-07-19t12:01:36z"
}
Node Unprovisioning is the process of removing a Node from the Mesh network.

## Slide 8
Gateway
Cloud
Node
LTE
BLE
Node Configuration
1. Node sends configuration information to Gateway
2. Gateway sends configuration info of node to cloud
Key | Value | Type | Range
JsonPacketId | 6 | Number | 0 - 99
GwySerNo | 1 | Number | 0 - 65536
NodeSerNo | 1 | Number | 0 – 65536
ElementAddr | 1 | Number | 0 – 65536
ErrorCode | 0 | Number | 0 - 6
Timestamp | "2022-07-19t12:01:36z " | String | 20 char long
Configuration status
Error code | Meaning
0 | Success
1 | Invalid GwySerNo
2 | Invalid NodeSerNo
3 | Invalid ElemAddr
4 | Invalid protocol
Error codes
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 6,
"GwySerNo": 2,
"NodeSerNo": 3,
“ElementAddr” : 5a,
“Errorcode” : 0,
"Timestamp": "2022-07-19t12:01:36z"
}
Node Configuration is the process in which the node is set to use a specific protocol for controlling the Air conditioner.
A provisioned node will be waiting in configuration mode until configured.
When a supported AC remote button is pressed in front of the node’s receiver, the node will get configured to act as that AC remote.

## Slide 9
Key | Value | Type | Range
JsonPacketId | 5 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65536
GwySerNo | 1 | Number | 0 - 65536
NodeSerNo | 1 | Number | 0 – 65536
ElementAddr | 5a | Number | 0 – 65536
Timestamp | "2022-07-19t12:01:36z " | String | 20 char long
Reconfiguration packet
Key | Value | Type | Range
JsonPacketId | 5 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65536
GwySerNo | 1 | Number | 0 - 65536
NodeSerNo | 1 | Number | 0 – 65536
ElementAddr | 5a | Number | 0 – 65536
ErrorCode | 0 | Number | 0 - 6
Timestamp | "2022-07-19t12:01:36z " | String | 20 char long
Reconfiguration ack
Error code | Meaning
0 | Success
1 | Invalid MsgSeqNo
2 | Invalid GwySerNo
3 | Invalid NodeSerNo
4 | Invalid ElemAddr
5 | Time out
Error codes
Gateway
Cloud
Node
1. Reconfiguration packet is sent from Cloud to Gateway
2. Reconfiguration packet is sent from cloud to gateway.
LTE
BLE
3a. If reconfiguratoin packet received from cloud has error, ack sent back to cloud with error code
3b. Node sends ack that it has entered configuration mode.
4. Gateway sends reconfiguration ack to cloud
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 5,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 5a,
"Timestamp": "2022-07-19t12:01:36z"
}
Node Reconfiguration
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 5,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 5a,
"ErrorCode": 0,
"Timestamp": "2022-07-19t12:01:36z"
}
Node enters configuration mode.
Node reconfiguration is the process in user can configure the node to use a different protocol from the one it was using before.

## Slide 10
Gateway
Cloud
Node
LTE
BLE
Control
Json packet (Cloud -> Gateway)
{
"JsonPacketID": 4,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 4,
“Power": 1,
“Mode": "Cool",
“Fan": 5,
“Temp": 25,
“SwingH": 1,
“SwingV": 1,
"OnTimer": 0,
"OffTimer": 0,
"Locking": 1
}
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 4,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
"ElementAddr": 4,
“Power": 1,
“Mode": "Cool",
“Fan": 5,
“Temp": 25,
“SwingH": 1,
“SwingV": 1,
"OnTimer": 0,
"OffTimer": 0,
"Locking": 1,
“Errorcode”: 0,
"Timestamp": "2022-07-19t12:01:36z"
}
1. Control packet is sent from the cloud
3a. If control packet received from cloud is invalid, control ack is sent back to the cloud with respective error code.
2. Control packet is sent to the node after parsing is successful
3b. Node sends control ack to Gateway
4. Gateway send control ack back to cloud

## Slide 11
Key | Value | Type | Range
JsonPacketId | 4 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65536
GwySerNo | 1 | Number | 0 - 65536
NodeSerNo | 1 | Number | 0 – 65536
ElementAddr | 1 | Number | 0 – 65536
Power | 1 = ON, 0 = OFF | Number | 0, 1
Mode | "Cool" | String | "Cool", "Hot", "Dry", "Auto", "Quiet"
Fan | 2 | Number | 0 – 4
Temperature | 25 | Number | 16 - 32
SwingH | 1 = ON, 0 = OFF | Number | 0, 1
SwingV | 1 = ON, 0 = OFF | Number | 0, 1
OnTimer | 4 | Number | 0 – 12
OffTimer | 5 | Number | 0 – 12
Locking | 1 = ON, 0 = OFF | Number | 1, 0
Timestamp | "2022-07-19t12:01:36z " | String | 20 char long
Control packet
Key | Value | Type | Range
JsonPacketId | 4 | Number | 0 – 99
MsgSeqNo | 1 | Number | 0 - 65536
GwySerNo | 1 | Number | 0 - 65536
NodeSerNo | 1 | Number | 0 – 65536
ElementAddr | 1 | Number | 0 – 65536
Power | 1 = ON, 0 = OFF | Number | 0, 1
Mode | "Cool" | String | "Cool", "Hot", "Dry", "Auto", "Quiet"
Fan | 2 | Number | 0 – 4
Temperature | 25 | Number | 16 - 32
SwingH | 1 = ON, 0 = OFF | Number | 0, 1
SwingV | 1 = ON, 0 = OFF | Number | 0, 1
OnTimer | 4 | Number | 0 – 12
OffTimer | 5 | Number | 0 – 12
Locking | 1 = ON, 0 = OFF | Number | 1, 0
ErrorCode | 0 | Number | 0 - 15
Timestamp | "2022-07-19t12:01:36z " | String | 20 char long
Control ack
Error code | Meaning
0 | Success
1 | Invalid GwySerNo
2 | Invalid NodeSerNo
3 | Invalid ElementAddr
4 | NodeSerNo – ElementAddr mismatch
5 | Invalid Power
6 | Invalid Mode
7 | Invalid Fan
8 | Invalid Temperature
9 | Invalid SwingH
10 | Invalid SwingV
11 | Invalid OnTimer
12 | Invalid OffTimer
13 | Invalid Locking
Error codes

## Slide 12
Gateway
Cloud
Node
LTE
BLE
Locking feature
1. Node detects that AC got controlled by its remote and Locking feature is enabled.
2. Gateway sends this information to cloud
Key | Value | Type | Range
JsonPacketId | 5 | Number | 0 - 99
MsgSeqNo | 1 | Number | 0 - 65536
GwySerNo | 1 | Number | 0 - 65536
NodeSerNo | 1 | Number | 0 – 65536
ElementAddr | 1 | Number | 0 – 65536
Timestamp | "2022-07-19t12:01:36z " | String | 20 char long
Locking status
Json ack (Gateway -> Cloud)
{
"JsonPacketID": 5,
"MsgSeqNo": 1,
"GwySerNo": 2,
"NodeSerNo": 3,
“ElementAddr”:5a,
"Timestamp": "2022-07-19t12:01:36z"
}
Node notifies the Gateway regarding this. After that sends the IR command to bring AC back to the state it was

## Slide 13
Json Packet Id | Meaning
0 | Gwy registration packet
1 | Gwy Unregistration packet
2 | Provisioning packet
3 | Unprovisioning packet
4 | Control packet
5 | Reconfiguration packet
6 | Configuration status packet
7 | Locking status packet
Reference Tables